## Slide 2: Components of Radar Signal Processing

## Slide 3: Components of Radar Signal Processing
Waveform Generator
  77 GHz waveform and required modulation for FMCW waveform
  Contains VCO (Voltage control Oscillator) which does the work of modulation as per required sensor parameters

## Slide 4: Components of Radar Signal Processing
Power Amplifier
  Amplify signal from waveform generator
  Provide enough power to reach the far away objects and also to get back to receiving antenna (100 m (MRR) or more than 250 m (LRR))

## Slide 5: Components of Radar Signal Processing
Transmitter antenna (Tx) and Receiving antenna (Rx)
  More than 1 transmitter Antenna and 2 or more receiving antenna are used
  More Receiving antenna, improves the angular resolution of the sensor and hence the overall perception efficiency of the sensor
  Distance between Antenna Array is different between different wavelength

## Slide 6: Components of Radar Signal Processing
Low Noise Amplifier (LNA)
  Amplifies the received signals at RX

## Slide 7: Components of Radar Signal Processing
Mixer
  Provides the Intermediate frequency (IF) which is further helps to find the distance of object from Radar in FFT
  Supports Digital Signal Processing block

## Slide 8: Components of Radar Signal Processing
Low Pass Filter and Analog to Digital Sampling
  Received signal is sampled and given further to DSP (Digital Signal Processor) available on the Radar ECU
  Tight with ECU processing power
  Supports Digital Signal Processing block

## Slide 9: Components of Radar Signal Processing
Digital Signal Processing
  Perform distance, speed and angle of the detected object and each of these parameters are measured for each reflected point (Detection).
  Involves Range – FFT, Doppler – FFT (2D FFT), CFAR, Angle of Arrival Determination, and finally Detection List generation for each Radar cycle
  Output will be used in Radar Data Processing (provide List of detections to compute List of Track Objects (ex: Clustering, Object Tracking, …)